## Slide 1
WEEK 13
Google Earth Engine
Cloud-Scale Time Series Analysis
ARIA v9.0 -- The Cloud Engine
Prof. Su Wen-Ray | National Taiwan University

## Slide 2
The Scale Gap
ARIA v9.0
W8–W12: Local Processing
W8
One Sentinel-2 scene, QGIS
W9
Two scenes, change detection
W10
SAR basics, one S1 image
W11
DEM + terrain analysis
W12
Random Forest, local ML
W13: Cloud Processing
Hundreds of images
Cloud-side computation
Time series analysis
Automatic compositing
Seamless export to local tools
1
image
→
2
images
→
10
images
→
500+
images

## Slide 3
Why Cloud Computing?
ARIA v9.0
☁
Scale
Your laptop has 16 GB RAM. Google Earth Engine has thousands of servers running in parallel. Process an entire country in minutes, not days.
↓
Zero Download
The data is already on Google's servers. No more waiting hours to download Sentinel scenes. You send commands; the data never leaves the cloud.
↻
Reproducibility
Your Python script IS your complete analysis workflow. Share the code, and anyone can replicate your results with zero setup.

## Slide 4
GEE Architecture
ARIA v9.0
PY
You
(Python / Jupyter)
GEE
Google
Servers
OUT
Results
(Map / CSV / GeoTIFF)
Commands →
→ Results
Server-Side Computation
Python sends instructions, not data.
Google's servers do all the heavy lifting.
Only the final result comes back to you.
Lazy Evaluation
Nothing executes until you request output.
Build a chain of operations first,
then trigger computation with .getInfo() or export.
Analogy: Like ordering at a restaurant -- the kitchen doesn't start cooking until you say 'That's my complete order.'

## Slide 5
Core Abstractions
ARIA v9.0
IMG
ee.Image
= One photo
A single raster with bands.
Sentinel-2 scene = one ee.Image
with 13 spectral bands.
IC
ee.ImageCollection
= Photo album
A stack of images filtered
by date, location, and
cloud cover.
Σ
ee.Reducer
= Statistical function
Collapses a collection
into one image: median,
mean, linearFit, etc.

## Slide 6
Python API + geemap
ARIA v9.0
No browser needed -- full GEE access from Python in Jupyter Notebook
import ee
import geemap
ee.Authenticate()
ee.Initialize(project='my-project')
Map = geemap.Map()
s2 = ee.ImageCollection('COPERNICUS/S2_SR_HARMONIZED')
.filterDate('2020-01-01', '2026-03-31')
.filterBounds(aoi)
.filter(ee.Filter.lt('CLOUDY_PIXEL_PERCENTAGE', 40))
Map.addLayer(s2.median(), vis, 'S2 Composite')
Map
geemap Features
Interactive maps in Jupyter
Layer inspector & drawing tools
Time series charts built-in
Export to GeoTIFF / CSV
Folium-style map controls
Works in VS Code & JupyterLab

## Slide 7
ARIA v9.0
Lab 1: NDVI Time Series
40 min hands-on
Sentinel-2 → Cloud Mask → NDVI → Monthly Aggregate → Plot
1
Filter Sentinel-2
filterDate(), filterBounds()
Cloud cover < 40%
2
Cloud Masking
Use SCL band to mask
clouds and shadows
3
Compute NDVI
normalizedDifference()
Map over collection
4
Monthly Statistics
Group by month, compute
mean / min / max
via combined Reducers
5
Band Chart + Spread
Shaded min-max band
+ spread bar chart
+ earthquake marker
Expected Output
Three-line chart: green mean + brown min (worst pixel) + dark-green max (best pixel)
Shaded band between min and max shows spatial spread across AOI
Lower panel: orange bar chart of spread (max-min) — widening = increased spatial heterogeneity
Earthquake marker at 2024-04-03 — compare: does min drop more than mean?
Key insight: mean dilutes local damage signals; min reveals localized landslide scars

## Slide 8
Median Composite: Why It Works
ARIA v9.0
50 Individual Images
Each has clouds in
different locations
Pixel-wise Median
For each pixel, take the
median across all 50 values
Cloud-Free Composite
Clouds are outliers →
median rejects them
automatically
➡
➡
Key Insight
Clouds appear randomly across images. The median of a pixel stack is almost always a cloud-free value because clouds are the outliers, not the norm. More images = better composite.
50
scenes
~70%
cloudy days
1
clean composite
<5 min
on GEE

## Slide 9
Three-Phase Composite Comparison (三期中值合成)
ARIA v9.0
Phase 1: Pre-EQ
震前基線
2023/01 – 2024/03
Baseline median composite
Healthy vegetation (NDVI 0.4–0.8)
15 months of imagery
Phase 2: Post-EQ
震後損害
2024/04 – 2024/09
Immediate earthquake damage
Landslides & exposed soil
NDVI drops (0.1–0.4)
Phase 3: Post-Dam
堰塞湖潰堤後
2025/10 – 2026/03
Landslide dam breach impact
New damage or partial recovery?
Multi-event tracking
→
→
Three ΔNDVI Maps — Disentangling Multi-Event Damage
delta_eq
Phase 2 − Phase 1
Earthquake direct damage
delta_dam
Phase 3 − Phase 2
Landslide-dam impact
(new damage or recovery?)
delta_total
Phase 3 − Phase 1
Total accumulated change

## Slide 10
Sentinel-1 in GEE
ARIA v9.0
S1
Complete S1 GRD Archive
GEE hosts the full Sentinel-1 Ground Range Detected (GRD) archive. Note: SLC data is not available in GEE -- only amplitude, not phase.
VV
VV Time Series
Cloud-independent monitoring! SAR penetrates clouds. Build VV backscatter time series for any location, any time period. Detect changes invisible to optical sensors.
W10
Connection to W10
Same SAR concepts from Week 10, now with temporal depth. Instead of one S1 image, analyze the full temporal stack. Speckle reduction via temporal averaging.
GRD
product type
VV+VH
polarizations
10m
resolution
6-day
revisit (2 sats)
2014+
archive start

## Slide 11
ARIA v9.0
Lab 2: SAR Time Series + Export
30 min hands-on
Sentinel-1 → VV Time Series → Pre/Post Composite → Export GeoTIFF
1
Filter S1 Collection
IW mode, VV polarization
Descending pass
filterBounds(aoi)
2
VV Time Series
Extract mean VV per date
Chart temporal profile
Identify change points
3
Pre/Post Composite
Temporal median composites
Before & after earthquake
Reduces speckle noise
4
Export GeoTIFF
ee.batch.Export.image
To Google Drive
Bridge to local tools
Bridge to Local Analysis
The exported GeoTIFF can be loaded directly into your W12 Random Forest classifier.
Cloud processing (GEE) produces clean inputs → local ML consumes them.
This is the real-world workflow: cloud for preprocessing, local for custom analysis.

## Slide 12
InSAR: Concept Introduction
ARIA v9.0
SAR Amplitude (W10)
How much energy bounced back
Measures surface roughness and geometry
Bright = rough surfaces (cities, forests)
Dark = smooth surfaces (water, roads)
Useful for land cover mapping
Available in GEE as GRD product
InSAR Phase (New!)
Timing of the return wave
Measures ground displacement
Compare phase of two SAR passes
Phase difference = distance change
Precision: millimeter-level!
Requires SLC data (not in GEE)
mm-Level Precision
InSAR can detect ground displacement as small as a few millimeters. This makes it invaluable for monitoring earthquakes, landslides, volcanic deformation, and subsidence.

## Slide 13
InSAR: Interferogram Reading
ARIA v9.0
Rainbow Fringes
Interferogram shows phase difference as color cycles.
Each complete color cycle (fringe) represents λ/2 displacement.
For Sentinel-1 (C-band, λ = 5.6 cm):
1 fringe = 2.8 cm of ground movement
4-Step Reading Method
1.
Satellite info -- which pass, which orbit?
2.
Count fringes -- how many full color cycles?
3.
Direction -- toward or away from satellite?
4.
Estimate displacement -- fringes × λ/2
Example Calculation
If you count 5 fringes in a Sentinel-1 interferogram: 5 fringes × 2.8 cm/fringe = 14 cm total displacement
This could indicate significant ground movement from an earthquake, landslide, or volcanic activity.
References
• 水保署電子報第141期 -- InSAR 地表變形監測
• 陳柔妃 & 林慶偉 (2018) -- InSAR 原理與應用

## Slide 14
InSAR: Tools & Resources
ARIA v9.0
Tool | Type | Best For
SNAP (ESA) | Desktop GUI | Beginners, single-pair interferograms
ISCE2 | Python CLI | Research-grade processing, full control
MintPy | Python package | Time series InSAR analysis
LiCSBAS | Python package | Large-scale time series with LiCSAR data
Data Sources
ASF DAAC
Alaska Satellite Facility
Full Sentinel-1 SLC archive
Free registration, bulk download
COMET LiCSAR
Pre-processed interferograms
Global coverage, auto-updated
Ready for time series analysis
Not covered in this course, but now you know where to start. These tools are your next step if you pursue SAR research.

## Slide 15
GEE vs STAC API
ARIA v9.0
 | Google Earth Engine | STAC API
Compute | Cloud (Google servers) | Local (your machine)
Scale | Massive (petabyte archives) | Limited by your hardware
Flexibility | Limited to GEE operations | Full control, any ML model
Data Access | GEE catalog only | Any STAC-compliant catalog
Setup | GEE account + ee.Initialize() | pip install + API endpoint
Export | GeoTIFF to Drive/Cloud | Direct download, xarray
Complementary, Not Competing
GEE excels at large-scale preprocessing, compositing, and time series over huge areas.
STAC API shines when you need custom ML pipelines, specific algorithms, or non-GEE data.
Best practice: use GEE for preprocessing → export → local analysis with full Python ecosystem.

## Slide 16
Cross-Week Integration
ARIA v9.0
GEE (W13)
Time series, composites,
export GeoTIFF
▼
Export GeoTIFF
W12: Random Forest
Classification using
GEE-exported composites
as input features
W10: SAR Fusion
Combine SAR temporal
stack with optical
composites
W9: Change Detection
Validate change maps
using multi-temporal
GEE composites
↙
↘
The Complete Workflow
GEE handles the heavy lifting (filtering, compositing, time series) → Export clean GeoTIFFs → Local tools (Python, QGIS) for custom analysis, ML, and visualization. Each week's skills feed into this pipeline.

## Slide 17
ARIA v9.0 Architecture
ARIA v9.0
Cloud Layer: Google Earth Engine
Sentinel-2 / Sentinel-1 archives → Filtering + Cloud Masking → Time Series & Composites → Export GeoTIFF
S2 Collection
S1 Collection
Cloud Mask
NDVI/VV Series
Median Composite
Export
▼ GeoTIFF ▼
Local Layer: Python / QGIS
rasterio
scikit-learn
Random Forest
Change Detection
QGIS Viz
ARIA Version History
v5.0
W8: First Light
v6.0
W9: Change Detection
v7.0
W10: SAR Integration
v7.5
W11: Terrain Engine
v8.0
W12: ML Classifier
v9.0
W13: Cloud Engine

## Slide 18
From Pixels to Petabytes
Reflection
1
Scale Changes Thinking
When you can process 500 images as easily as 1, you design different analyses. Think in time series, not single scenes.
2
Cloud + Local = Complete
Cloud computing handles the heavy lifting. Local tools give you full control. The best workflow combines both.
3
Question Your Statistics
The mean can hide local damage. Adding min/max revealed what the average missed. The best skill in data science is asking better questions.
ARIA v9.0 -- The Cloud Engine
Prof. Su Wen-Ray | National Taiwan University
ARIA v9.0